## Slide 1
CPU Execution Lab
Session 1: Setup and systems foundations
CAIR Tenstorrent Blackhole Project, September 15, 2026
Notes: Open by framing this as a setup and shared-language session. The code repository and assignment directions will follow after the lecture.

## Slide 2
Session plan
Confirm that everyone has the tools needed for the lab
Build a simple model of CPU execution and memory
Preview the experiments that will become the shared benchmark
Connect the CPU observations to machine learning and Blackhole
2
Notes: Keep the scope clear. Students do not need to program Blackhole today. They need enough systems vocabulary to understand why later accelerator work cares about instructions, locality, and parallel work.

## Slide 3
Setup checklist
Git is installed and prints a version
Visual Studio Code opens normally
A terminal opens and accepts commands
At least one C compiler prints a version
Your GitHub fork exists and its local clone opens in VS Code
Lab 1 does not require CMake, Python packages, a GPU, or a Tenstorrent card
3
Notes: Use setup.md as the source of truth. The shared minimum is Git, an editor, a terminal, and a C compiler. Students may have different operating systems and different compiler names.

## Slide 4
Opening your cloned fork in VS Code
Open the Visual Studio Code application
Select File > Open Folder
Find the location where you cloned your fork
Select the main blackhole folder, then open it
Confirm that README.md and the labs folder appear in the Explorer
Select Terminal > New Terminal, then run git status
WSL: open Ubuntu, enter the cloned repository, and run code .
VS Code may ask you to install its WSL extension.
4
Notes: Students should open the repository root, not only the lab subfolder. Opening the root makes the full project structure and Git status available. For WSL, code . opens the current Linux folder in VS Code through the WSL integration.
Sources:
https://code.visualstudio.com/docs/terminal/basics
https://code.visualstudio.com/docs/remote/wsl

## Slide 5
Three copies of the repository
Original repository
rvfvn/blackhole
Your GitHub fork
your-username/blackhole
Your local clone
the folder stored on your computer
These copies change only when GitHub or Git synchronizes them.
5
Notes: Name the three locations clearly. The original repository is commonly called upstream. Their GitHub fork is commonly called origin after they clone it. The local clone is the folder where they edit and compile. A change in one location does not automatically appear in the other two.
Source: https://docs.github.com/en/get-started/git-basics/managing-remote-repositories

## Slide 6
Keeping your fork current
First, update the fork on GitHub
Open your fork, select Sync fork, then select Update branch.
Next, update the local clone in the VS Code terminal
git switch main
git pull origin main
A plain git pull usually checks your fork. It cannot retrieve new upstream files until the fork has been synchronized.
6
Notes: Students who cloned their fork usually have origin pointed at that fork. Git pull therefore retrieves changes already present in the fork. The GitHub Sync fork action first brings changes from rvfvn/blackhole into their fork. The two terminal commands then update the local main branch. Ask students to sync before creating a new work branch. If GitHub reports a conflict, pause and ask for help.
Source: https://docs.github.com/en/pull-requests/how-tos/work-with-forks/syncing-a-fork

## Slide 7
Compiler setup on macOS and Linux
macOS
xcode-select --install
Ubuntu or Debian
sudo apt update
sudo apt install git build-essential
Verify after installation
git --version
cc --version
7
Notes: On macOS, the Xcode Command Line Tools package provides Clang and other command-line development tools. On Ubuntu or Debian, build-essential provides the standard build toolchain. Other Linux distributions use different package managers.
Source: https://developer.apple.com/documentation/xcode/installing-the-command-line-tools

## Slide 8
Windows setup with WSL
Check in PowerShell or Windows Terminal
wsl --status
wsl --list --verbose
Install WSL when it is missing
wsl --install
Then open Ubuntu and install the lab tools
sudo apt update
sudo apt install git build-essential
8
Notes: WSL gives Windows students a Linux command-line environment, which keeps the lab commands consistent across the group. A restart may be required after installation. Native Windows toolchains may also work, but WSL is the recommended course path.
Source: https://learn.microsoft.com/en-us/windows/wsl/install

## Slide 9
Build and run preview
After the repository is posted, compile from the lab folder:
cc -std=c11 -O2 -Wall -Wextra -pedantic
-Iinclude src/*.c -o cpu_lab
Run the executable:
./cpu_lab
The terminal will print results from each benchmark experiment.
9
Notes: Explain only the purpose of the command today. cc invokes the available C compiler, the flags request C11 and warnings, -O2 enables optimization, -Iinclude adds the header folder, and src/*.c selects the source files. CMake is optional and not part of the student workflow.

## Slide 10
The CPU
The CPU is the computer's general purpose processor
It executes streams of machine instructions
Registers hold values currently used by instructions
Arithmetic units perform operations such as addition and multiplication
Caches keep recently used data close to the processor
10
Notes: Avoid presenting the CPU as literally doing only one instruction at a time. Modern CPUs overlap and reorder work. The beginner model is that programs become instruction streams operating on values and memory.
Source: https://pages.cs.wisc.edu/~markhill/cs354/Fall2008/notes/basics.html

## Slide 11
From C source to a running process
1. You write a C source file.
2. The compiler creates machine code and an executable.
3. The operating system starts a process and maps its code and data into memory.
4. The CPU fetches and executes the program's instructions.
The source code is for humans. The executable is for the machine.
11
Notes: This is the small amount of operating-system context the lab needs. A process is a running instance of the program with memory and operating-system resources. Keep details such as virtual memory and scheduling for later sessions.

## Slide 12
Machine instructions
Load: bring a value from memory into a register
Store: write a value from a register back to memory
Arithmetic: add, multiply, or update an address
Compare and branch: decide whether a loop continues
Registers: small named locations used directly by the CPU
12
Notes: Students only need to recognize categories. They do not need to memorize an instruction set. Later, the assembly view will show these categories in compiler output.

## Slide 13
The practical memory hierarchy
Registers
A few values used directly by current instructions
Caches
L1, L2, and often L3 keep nearby or recently used data
DRAM
Larger working memory for running programs
Accessing data from farther levels usually costs more time.
13
Notes: The exact cache design varies across machines. The useful model is distance and capacity: small storage near compute is quick to access, while larger memory is farther away. Hardware moves blocks called cache lines, so nearby addresses often help.
Source: https://www.cs.cornell.edu/courses/cs3410/2024fa/notes/caches.html

## Slide 14
The lab question
How much can performance change when the computation stays the same but the data moves differently?
We will change access order, layout, and work division. Then we will measure the result.
14
Notes: This is the central question for every experiment. Keep returning to it. Students should separate mathematical work from the path data takes through the machine.

## Slide 15
Memory access experiments
Strided access: touch the same array with different gaps between elements
Row and column traversal: visit the same matrix in two orders
Bandwidth copy: measure the cost of moving a large block of data
The total data can stay similar while the access pattern changes
15
Notes: Connect each experiment to one observation. Stride shows locality. Row and column traversal shows how a two-dimensional idea maps to linear memory. Bandwidth copy shows that movement itself consumes time.

## Slide 16
Benchmarking carefully
Check that every implementation produces the expected result
Test several input sizes
Run each case more than once
Use the same compiler settings for comparisons
Compare patterns on one machine before comparing different machines
Record unusual conditions such as heavy background activity
16
Notes: Timing results will vary across CPUs, operating systems, compilers, and power settings. In the code, allocate memory outside the timed region, use a monotonic clock, and consume results so the compiler cannot remove the work. The goal is a repeatable pattern, not one universal timing number.

## Slide 17
Matrix multiplication
C[i,j] = Σ A[i,k]B[k,j]
Each output value is a dot product
The inner loop repeats multiply and add operations
Many machine learning layers contain matrix multiplication
A useful shorthand is input multiplied by weights
17
Notes: Work a tiny example verbally if needed, such as one row of A dotted with one column of B. Matmul matters here because it combines regular arithmetic with repeated data access, making it useful for both machine learning and architecture discussions.
Source: https://docs.tenstorrent.com/tt-metal/latest/tt-metalium/tt_metal/labs/matmul/lab1/lab1.html

## Slide 18
Naive and transposed matmul
Naive access
A[i][k] reads across a row
B[k][j] jumps between rows
Transposed access
A[i][k] reads across a row
BT[j][k] also reads across a row
The mathematical result stays the same. The memory access pattern changes.
Measure transpose cost separately or state clearly when the benchmark excludes it.
18
Notes: In row-major storage, varying k in B[k][j] steps by an entire row. Using a pre-transposed B makes the inner reads contiguous. Be honest about setup cost: a one-time transpose has a cost, but repeated matrix multiplications may amortize it. Floating-point results can also differ slightly when operation order changes.
Source: https://docs.tenstorrent.com/tt-metal/latest/tt-metalium/tt_metal/labs/matmul/lab1/lab1.html

## Slide 19
Assembly view
cc -std=c11 -O2 -Iinclude -S src/stride_access.c
-o stride_access.s
Register names
Load and store instructions
Arithmetic instructions
Compare and branch instructions
Repeated instruction groups that form loops
19
Notes: Assembly differs across x86 and Arm machines, and compilers may optimize the same C code differently. Ask students to identify categories and loop structure. Do not turn this into an instruction-set memorization exercise.

## Slide 20
Optional threading experiment
Divide a large array into separate ranges
Let each thread compute one partial sum
Combine the partial sums after all threads finish
Thread creation and coordination also consume time
Parallel work helps when the task is large enough and divides cleanly
20
Notes: This experiment introduces work division without requiring deep operating-system coverage. Threads share the process memory. The operating system schedules them, and available CPU cores determine how much can truly run at once. Keep it optional because threading support and performance vary across platforms.

## Slide 21
Why AI accelerators exist
Machine learning workloads repeat large amounts of regular numerical work
Specialized matrix and vector engines can process that work efficiently
Local memory can keep reused data close to compute
Many workers can process independent pieces of a larger tensor
A fast interconnect and memory system must keep those workers supplied
21
Notes: Avoid saying that CPUs are bad or obsolete. CPUs excel at general-purpose control and varied workloads. Accelerators add hardware organized around regular, high-throughput numerical computation, where data supply and reuse matter as much as arithmetic.

## Slide 22
After the lecture
Open your GitHub fork and use Sync fork
In the local clone, switch to main and pull from origin
Follow setup.md for your operating system
Confirm that the lab builds and runs from the terminal
Create a work branch for the assigned benchmark or project role
Submit the completed contribution through a pull request
22
Notes: The repository post should repeat the exact synchronization and branch commands. Students should update main before they create a work branch. Each contribution should fit the shared interface so that the group work compiles into one benchmark executable.

## Slide 23
Blackhole preview
RISC-V processors coordinate device work
Local L1 SRAM keeps working data near compute
The Network-on-Chip moves data across the device
Specialized matrix and vector engines operate on tensor data
GDDR6 stores larger data on the device
Today's CPU lab gives us four questions: What computes? Where does data live? How does it move? How is the work divided?
23
Notes: End here. Blackhole makes data placement, movement, and parallel work more explicit. Students do not need the internal details yet. The CPU experiments give them concrete observations that later map to local SRAM, NoC transfers, Tensix cores, RISC-V control, and matrix or vector engines.
Sources:
https://docs.tenstorrent.com/tt-metal/latest/tt-metalium/tt_metal/labs/matmul/lab1/lab1.html
https://docs.tenstorrent.com/aibs/blackhole/installation.html
https://docs.tenstorrent.com/tt-metal/latest/tt-metalium/tt_metal/advanced_topics/compute_engines_and_dataflow_within_tensix.html